## Slide 1
Modern Clocking Strategies:
Adaptive Clocking
Jordi Cortadella Universitat Politècnica de Catalunya

## Slide 2: Outline
Sources of variability
  Static/dynamic, local/global
Reducing Margins for Static and Slow Variability
  Binning
  Voltage-Frequency Scaling
Reducing Margins for Fast Variability
  Resilient circuits
  Adaptive Clocks
Reactive Clocks and GALS

## Slide 3: The cost of variability
margins
frequency

## Slide 4: The cost of variability
margins
frequency
Goal:
Reduce margins
Impact:
Speed Energy

## Slide 5: Process variability
Fast
Typical
Slow

## Slide 6: Dynamic variability
Raj Nair (Anasim Corp.), IC floorplanning and Power Integrity, SOCcentral, Aug 2, 2010.
http://www.soccentral.com/results.asp?entryID=31901. From SOCcentral.com, Copyright 2002 - 2014 Tech Pro Communications
(Vdd-Vss)
Dynamic variability (V,T) depends on the actual activity of the circuit
Assumptions required on the min/max values for voltage and temperature
Ranges may depend on the application domain (automotive, HPC, handheld devices, …)

## Slide 7: Global and local variability
Source: H. Masuda et al. (ICICC 2005) Challenge: Variability Characterization and Modeling for 65- to 90-nm Processes
D2D (global)
WID (local)

## Slide 8: Timing
Combinational Logic
Flip Flops
Flip Flops
PLL

## Slide 9: Timing: setup constraint
1
2
1
1
2
Comb. Logic
Two competing paths:
Launching path
Capturing path
Launching path < Capturing path + Period
2
PLL
PVTA variability
No variability (or very little)
+ Margins

## Slide 10: Margins for Variability
Period
launching path
Q
D
D
Q
time
capturing path

## Slide 11: Margins for Variability
Q
D
D
Q
Period
clock-data compensation
launching path
margin
capturing path
Q
D
D
Q
Period
time
Margins are required to account for the worst-case variability (static and dynamic)
Is there room to reduce margins?
Voltage droop

## Slide 12: Variability and margins
 | Static | Dynamic | 
 |  | Slow (ms) | Fast (ns)
Global (corners) | PV | VTA | V
Local (OCV) | PV | VTA | V
Voltage variability:
  Static IR drop
  Dynamic IR drop
  Inductive noise (Ldi/dt)
(P:Process; V: Voltage; T: Temperature; A: Aging)

## Slide 13: Reducing Margins for Static and Slow Variability

## Slide 14: V-F operation points
Voltage
Frequency

## Slide 15: V-F operation points
Voltage
Frequency
Nominal voltage

## Slide 16: Speed binning
Voltage
Frequency
Nominal voltage

## Slide 17: Voltage binning
Voltage
Frequency

## Slide 18: Dynamic Voltage Frequency Scaling (DVFS)
Voltage
Frequency
DVFS Table | 
DVFS Table | 
Open loop control (SW).
(V,F) selected according to:
  Workload
  Temperature
  Power budget

## Slide 19: DVFS scheme
DVFS block
L-SHIFTERS & CDC
V1
VRM
V2
VRM
(variable)
(fixed)
SW

## Slide 20: AVS scheme
AVS block
V1
VRM
V2
VRM
(variable)
(fixed)
PMU
L-SHIFTERS & CDC
Performance Monitor
Closed Loop Control
Every die works at its best (V,F) point (plus some guardband margins)
AVS can compensate slow variability (temperature, aging)

## Slide 21: Performance monitors
Estimate the voltage/frequency relationship of the actual silicon
Examples:
Counter
Ref. Clock
Measure frequency
Ring oscillator
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
CLK
delay
Edge detector
Time-to-digital converter

## Slide 22: Reducing Margins for Fast Variability

## Slide 23: Resilient circuits
CLK
Data
CLK
CLK_del
Data
P
P + 
Error recovery
Different values
Conventional timing
Resilient timing
=
Error
Main flip-flop
Shadow latch
delay
Main data
Shadow data
CLK
Data

## Slide 24: Resilient circuits
Source: D. Ernst et al., Razor: circuit-level corrrection of timing errors for low-power operation,
IEEE Micro, Nov-Dec 2004.

## Slide 25: Resilient circuits: technical issues
CLK
CLK_del
Data
P
P + 
Potential metastability

min short path
Error recovery
(may take several cycles)
Only critical flip-flops require shadow latches
Short paths must have a min delay
Metastability may take several cycles to resolve
Sophisticated error-recovery procedures are required

## Slide 26
Source: S. Das et al., RazorII: In Situ Error Detection and Correction for PVT and SER Tolerance. IEEE JSSC 44(1), Jan 2009.

## Slide 27: Resilient circuits
Resilient circuit
Vdd
VRM
Error Monitor
Closed Loop Control
probability of error
num cycles for error recovery
Closed Loop Control:
  Raise voltage if too many errors
  Lower voltage if too few errors
Error recovery mechanism:
  Reuse existing checkpoint schemes in advanced processors

## Slide 28: Schemes with resilient circuits
ARM + University of Michigan
  Different variations: Razor I, Razor II, Bubble Razor
Intel:
  Transition Detector with Time Borrowing (TDTB)
  Double Sampling with time Borrowing (DSTB)
Using pausable clocks and metastability detectors
  SafeRazor (Torino, Technion and UPC)
  Blade (USC)

## Slide 29: Voltage droops
Source: Y. Kim et al., Automating Stressmark Generation for Testing Processor Voltage Fluctuations,
IEEE Micro, July-August 2013.
Voltage droops are the main source of fast variability

## Slide 30: Power Delivery Network
Source: Jitesh Shah
Floorplanning A Power Delivery Network With Spice Electronic Design
July 24, 2008 http://electronicdesign.com/energy/floorplanning-power-delivery-network-spice

## Slide 31: PDN model
Local Global

## Slide 32: Adaptive Clock
Vdd
Droop detected
Period stretched
New frequency
Mechanisms are needed for:
  Droop detection
  Clock period stretching
  Frequency reduction
DLL
CLK

## Slide 33: AMD Steamroller
Source: K. Wilcox et al. Steamroller Module and Adaptive Clocking System in 28nm CMOS IEEE JSSC 50(1), Jan 2015.

## Slide 34: Intel Adaptive Clock
Source: K.A. Bowman et al. A 22 nm All-Digital Dynamically Adaptive Clock
Distribution for Supply Voltage Droop Tolerance,
IEEE JSSC 48(4), April 2013.

## Slide 35: Intel Adaptive Clock

## Slide 36: Margins for Adaptive Clocks
Clk
Nominal voltage
droop detection threshold
Reaction time
margins saved by adaptive clock
Circuit
Sensors
Frequency Synthesizer
Control
Other approaches:
N. Kurd, P. Mosalikanti, M. Neidengard, J. Douglas, and R. Kumar, Next generation Intel core micro-architecture (Nehalem) clocking, IEEE JSSC 44(4), 2009.
K. Chae and S. Mukhopadhyay, All-digital adaptive clocking to tolerate transient supply noise in a low-voltage operation, IEEE TCAS II 59(12), 2012.
C. Lefurgy, A. Drake, M. Floyd, M. Allen-Ware, B. Brock, J. Tierno, J. Carter, and R. Berry, Active guardband management in Power7+ to save energy and maintain reliability, IEEE Micro 33(4), 2013.

## Slide 37: Reactive Clocks

## Slide 38: Mechanisms to reduce margins
 | Static | Dynamic | 
 |  | Slow (ms) | Fast (ns)
Global (corners) | PV | VTA | V
Local (OCV) | PV | VTA | V
Mechanism | Reduces margins for …
Binning, DVFS (open loop) | Static variability
AVS (close loop) | + Slow global variability
Adaptive Clocks | + Fast global variability (moderate)
Reactive Clocks | + Fast global variability (aggressive)
Resilient circuits | Any variability (aggressive)

## Slide 39: Timing: setup constraint
1
2
1
1
2
Comb. Logic
Two competing paths:
Launching path
Capturing path
Launching path < Capturing path + Period
2
PLL
PVTA variability
No variability (or very little)
+ Margins

## Slide 40: Reactive Clock
Comb. Logic
Launching path < Capturing path + Period
PVTA variability
+ Margins
Correlated!
PLL

## Slide 41: Variability: PLL vs. Reactive Clock
PLL period
launching path
Q
D
D
Q
time
capturing path

## Slide 42: Variability: PLL vs. Reactive Clock
Q
D
D
Q
PLL period
Q
D
D
Q
Reactive Clock
clock-data compensation
launching path
margin
capturing path
Q
D
D
Q
PLL period
time
Voltage droop

## Slide 43: PLL vs. Reactive Clock
Reactive Clk (1.2V)
Reactive Clk (0.85V)
30%
PLL (1.2V)
Vdd = 1.2V  30%
Fixed frequency
Adaptive frequency

## Slide 44: Reactive Clock
Reactive Clock
PLL
Enable
Gain: 40% less Energy or 1.6x speed-up
Pain: Negligible
Risk: Zero
Original circuit not modified
Negligible area
Post-tapeout calibration (by SW)
Conventional timing (PrimeTime)
Clock domain
J. Cortadella, L. Lavagno, P. López, M. Lupon, A. Moreno, A. Roca, and S. S. Sapatnekar. Reactive clocks with variability-tracking jitter. ICCD 2015.

## Slide 45: PLL vs. Reactive Clocks
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)

## Slide 46: PLL vs. Reactive Clocks
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
Timing sign-off
SPICE models (65nm)
Slow 125oC

## Slide 47: PLL vs. Reactive Clocks
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)
Slow 125oC
Typical 125oC
Timing sign-off
Ideal binning

## Slide 48: PLL vs. Reactive Clocks
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)
Timing sign-off
Slow 125oC
Typical 125oC
Slow 75oC

## Slide 49: PLL vs. Reactive Clocks
PLL
Rclk
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)
Slow 125oC
Typical 125oC
Timing sign-off
Slow 75oC
Typical 75oC

## Slide 50: PLL vs. Reactive Clocks
PLL
Rclk
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)
Slow 125oC
Typical 125oC
Timing sign-off
Slow 75oC
Typical 75oC
1.6x
1.2x
and great benefits for hostile environmental conditions (> 2x)

## Slide 51: PLL vs. Reactive Clocks
sign-off
PLL
Rclk
DUT
PLL
Rclk
temperature
25oC
125oC
75oC
SPICE models (65nm)
slow die
typical die
-20% (1.07V)
-42% (0.91V)
Energy reduction (@iso-performance)

## Slide 52: Synthesis of the Ring oscillator
Library Corners
Critical paths
PLL period
Delay
OCV
Programmable by SW

## Slide 53: Reactive Clock Domain
PLL
Enable
Clock domain
CDC
CDC
CDC
Ring oscillator
CDC structures required for communication outside the clock domain

## Slide 54: GALS with Reactive Clocks
RO
RO
RO
RO
A different Reactive Clock for each domain
Clock Domain Crossing structures between domains

## Slide 55: Summary
Ideal typical die (no PVT variability)
Slow die (sign-off)
Binning (or AVS)
Adaptive clock (tolerance to droops)
Resilient (Razor)
Reactive clock (ring oscillator)
Typical dies

## Slide 56: Conclusions
Moore’s law is (economically) over. It is time to exploit what is left in established nodes.
What is left? Margins for variability.
Dilemma: how to spend your money?
  introducing techniques to reduce margins, or
  moving to a new (expensive) technology node