## Slide 1: Making Petri nets friendlier to designers
Jordi Cortadella (Universitat Politècnica de Catalunya, Barcelona)
STRUCTURE 2017

## Slide 2: Outline
Friendly specification models for asynchronous circuits
Mining friendly process specifications

## Slide 3: Friendly specification models for asynchronous circuits
Jordi Cortadella, Alberto Moreno, Danil Sokolov, Alex Yakovlev, and David Lloyd. Waveform transition graphs: a designer-friendly formalism for asynchronous behaviours. Int. Symp. on Advanced Research in Asynchronous Circuits and Systems, May 2017.

## Slide 4: Specification of an asynchronous circuit
Inputs
Outputs
Minimalist Petri net (Signal Transition Graph)

## Slide 5: Asynchronous controllers
Source: Sokolov et al., Towards asynchronous power management, FTFC 2014.

## Slide 6: Specification formalisms: process algebras
procedure buffer (input i: byte; output o: byte) is variable x : byte begin loop i -> x ; o <- x end end
Balsa:
Set Env = { rinp, routp, ainp, aoutp };
agent Env-L = rin.’rinp.Env-Lw;
agent Env-Lw = ainp.(‘ain.Env-L + ainp.Env-Lw);
agent Env-R = routp.(‘rout.aout.’aoutp.Env-R + routp.Env-R);
agent Implementation = (Env-L | Circuit | Env-R) \ Env;
CCS:

## Slide 7: Specification formalisms: Burst Mode
s1
s2
a+, b-/ x-, y+
No input/output concurrency

## Slide 8: Specification formalisms: STGs
Device
lds
ldtack
d
dsr
dsw
dtack
VME Bus
Controller
Data
Transceiver
Bus

## Slide 9: STGs are great !
Any asynchronous behaviour can be specified.
Implementation properties can be easily checked:
  Consistency, output persistence, state encoding.
There is a solid automatic synthesis flow from STGs to circuits (e.g., petrify, MPSAT):
  State encoding
  Logic synthesis for speed-independent circuits
  Logic decomposition and technology mapping

## Slide 10: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 11: Control specification
Ri
Ro
Ao
Ai
FIFO
cntrl
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-

## Slide 12: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 13: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 14: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 15: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 16: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 17: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 18: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 19: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 20: Control specification
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl
Ri
Ro
Ai
Ao
C
C

## Slide 21: Trying to persuade engineers (the cruel reality)
Yeah! Signal Transition Graphs are extremely useful.
They are based on Petri nets!.
They have places, transitions, and some tokens that flow, …
petri what …? tokens?

## Slide 22: We need a simpler formalism
STGs
?
STG experts
Non-expert engineers

## Slide 23: Wish list for the specification model
Easy adoption.
Powerful
  maybe a little bit less than STGs
  but more than Burst Mode
Efficient: use logic synthesis (Boolean minimization).
Reuse the existing infrastructure for STGs.
STGs
?

## Slide 24: Engineers understand waveforms
Source: Xilinx LogiCORE IP FIFO Generator

## Slide 25: Multiple waveforms (modes of operation)
Choice

## Slide 26: Expressive power
Causality and concurrency between events.
Choice (modes of operation):
  AMBA bus: read/write cycle.
Proposal (our sacrifice):
  Concurrency and choice mutually exclusive.
STGs
?

## Slide 27: Expressive power
Not allowed

## Slide 28: Example: Buck controller

## Slide 29: Mode: UV before ZC
zc
uv
oc
gp
gp_ack
gn
gn_ack
no concurrency
no concurrency

## Slide 30: Waveform Transition Graph (WTG)
WF
WF
WF
WF
WF
(nodal states)
choice-free & acyclic

## Slide 31: Waveform Transition Graph (WTG)
WF
WF
WF
WF
WF
(nodal states)
choice-free & acyclic

## Slide 32: Nodal state in reachability graph
w
w
x
x
y
y
z
z
a
b
b
c
c
d
d
e
e
nodal state (no concurrency)
Only nodal states can have choice
For timed verification: all counters to zero

## Slide 33: Waveform Abstraction
Causality & Concurrency (choice-free)
Silent transitions might be acceptable

## Slide 34: WTG of a buck controller
WF1
WF2
WF3

## Slide 35: Concurrency and choice
Device
LDS
LDTACK
D
DSr
DSw
DTACK
VME Bus
Controller
Data
Transceiver
Bus

## Slide 36: Concurrency and choice
Device
LDS
LDTACK
D
DSr
DSw
DTACK
VME Bus
Controller
Data
Transceiver
Bus
DSr
LDS
LDTACK
D
DTACK

## Slide 37: Concurrency and choice
Device
LDS
LDTACK
D
DSr
DSw
DTACK
VME Bus
Controller
Data
Transceiver
Bus

## Slide 38: WTG for the VME bus controller
WF read
WF write

## Slide 39: WTG: expressive power
STG
BM
WTG

## Slide 40: BM vs. WTG vs. STG
S1
S2
a+,b-/ x-,y+
S1
S2
BM
STG
WTG

## Slide 41: Structural properties of SC WTGs
WF
WF
WF
WF
WF
choice-free & acyclic
Reachability (conjecture):
Negative result (not tragic): Safe Marked Graphs  WTG
Live
Safe
Abstraction: one State Machine
Every cycle of the RG contains at least one nodal state
WF (acyclic)

## Slide 42: Not every safe Marked Graph is a WTG
a
b
x
y
Every state is at one side of some diamond
u
u
v
v
a
a
b
b
b
b
y
y
y
y
x
x
No nodal state

## Slide 43: Mining friendly process specifications
Javier de San Pedro and Jordi Cortadella. Mining structured Petri nets for the visualization of process behavior. 31st ACM Symposium on Applied Computing, April 2016.

## Slide 44: Mining specifications
Log:
a b c d e a b a c d b e c b a c b d e a b a b c e a a d e c a c b e c a d e a
a
a
a
a
b
b
b
c
c
c
c
c
b
b
d
d
d
e
e
e
d

## Slide 45: From LTS to Labelled Petri Net
LTS
LTS
Overfitting vs. Underfitting
Spaghetti models
Flower models ()

## Slide 46: Our proposal
Log
Discovery
Model
Slicing
Log slice 1
…
Discovery
Model 1
Log slice n
Discovery
Model n
…
Process behavior
Model
Model 1
Process behavior
Model
Model 2
Process behavior
Model 3
Few models, each is low-complexity
Discovery

## Slide 47: Extracting well-structured slices
Most frequent behavior
Less frequent
Slicing
Captures more than 90% of log

## Slide 48: Mining specifications
Log:
a b c d e a b a c d b e c b a c b d e a b a b c e a a d e c a c b e c a d e a
a
a
a
a
b
b
b
c
c
c
c
c
b
b
d
d
d
e
e
e
d

## Slide 49: Slicing specifications
a
a
a
a
b
b
b
c
c
c
c
c
b
b
d
d
d
e
e
e
Log:
a b c d e a b a c d b e c b a c b d e a b a b c e a a d e c a c b e c a d e a
Best and Devillers:
  Characterisation of the state spaces of marked graph Petri nets
  Synthesis of live and bounded persistent systems
Petrify  Synthesis of free-choice Petri nets
SAT formulation
d

## Slide 50: Slicing specifications
a
a
b
b
b
c
c
c
c
b
b
d
e
e
a
a
c
d
d
e
Log:
a b c d e a b a c d b e c b a c b d e a b a b c e a a d e c a c b e c a d e a
d

## Slide 51: Slicing specifications
Log:
a b c d e a b a c d b e c b a c b d e a b a b c e a a d e c a c b e c a d e a
71%
29%
Monolithic Petri net

## Slide 52: SAT model
a
b
c
b
c
d
b
c
b
c
e
e
Log:
a b c e
a c b e
a d b c e
One Boolean variable per LTS transition
  is true if corresponding arc is selected in slice
Every valid assignment forms an LTS slice (subset)

## Slide 53: Example: forward persistence
a
b
c
b
c
d
b
c
b
c
e
e
Log:
a b c e
a c b e
a d b c e
Forward persistence:
  If a and b exist in a LTS slice, then a and b must exist too.
b
a
b
a
SAT constraints:

## Slide 54: Example: forward persistency
a b c e
a c b e
a d b c e
a b c e
a c b e
a d b c e

## Slide 55: Example: incidenttelco
Petri net mined with ILP miner:
448 arcs
9800 crossings
100% fitness

## Slide 56: Example: incidenttelco
65 slices required for 100% fitness
However, with the first slice only:
Original
448 arcs
9800 crossings
100% fitness
1st slice
15 arcs
Planar (0 cros.)
92.6% fitness
Covers most behaviours

## Slide 57: Other examples
Similar results in other benchmarks
  Only 1-3 slices required for >90% of behaviour
  Every slice is low visual complexity
Benchmark | # of slices | # of crossings
documentflow | 1 | 0
fhmilu | 1 | 4
fhmn5 | 1 | 1
incidenttelco | 1 | 0
kim | 1 | 0
purchasetopay | 1 | 0
receipt | 1 | 3
tsl | 3 | 3
# of slices | # of crossings
4 | 8
1 | 4
1 | 1
2 | 1
2 | 0
1 | 0
1 | 3
10 | 9
For >95% of behaviour

## Slide 58: Conclusions
We need to expand the social circle of Petri nets:
  Asynchronous circuits
  Process/Specification mining
  … and many other domains
Simple structures contribute to sympathise with Petri nets:
  For specification (WTG)
  For analysis and visualisation (Petri net slices)
The structural theory of Petri nets is an essential guidance:
  “Nice” commonly means “visually friendly”
  Correlation between structural properties and visualisation